## Slide 1: UI & Schedule Format for Auto Box Test
Version 2.01
New Feature Release

## Slide 2: New Feature Introduction
Image Comparison function and comparison result report.
Add Pause button.
Add Preview camera video.
Add timer button and Schedule Timer list.
Add progress bar.
Modify UI program style.
Drop-down list of RC key.
Add unknown camera manual setting.
On line schedule edit and save function.
Release Script Template V2.01.

## Slide 3: UI Introduction - Main Screen
New feature:
Save as schedule file
Switch Schedule
Schedule RC key info
Change Serial port
Camera
Video
Log
Data
New feature:
Start / Pause stress test
New feature:
Preview camera video
Enter setting page
Schedule
Command

## Slide 4: UI Introduction - Main Screen
Test time of schedule
Total loop / Current loop
Schedule
Timer
New feature:
drop-down list of RC key
New feature:
Pop Schedule Timer list
New feature:
Schedule progress bar
New feature:
IF you set Schedule Timer, schedule will auto to start,
user does not need to press [START ] button.
Version info

## Slide 5: UI Introduction – Main Setting
Select location to save photo and log, load RC DB.
Camera setting, select your camera device.
RedRat setting, select RedRat database.
Secord RS232 setting, select your comport and baudrate.
Press “SAVE” button to save date
New feature:
User can add camera data manually.

## Slide 6: UI Introduction – Multi Schedule Setting
Setting how many times to test for a schedule.
Press to load schedule file.
Video record after each schedule finished.
Press “SAVE” button to save date.
New feature:
Start time of schedule.
New feature:
Similarity of Image Comparison.
New feature:
Enable or not to run schedule.

## Slide 7: UI Introduction – Mail Setting
Enable or not to send mail after stress test finished.
If you enable it, [Form] and [To] must be filling in data.
Filling in information for mail.
Press “SAVE” button to save date
New information:
Project number of URTracker.

## Slide 8: Schedule Example
System Setting :
Working folder setting
Input the schedule description
Execute by test times
Soft Remind:
Please use Script Template V2.01.xlsx to edit Schedule
If want use old Schedule, please transform new format

## Slide 9: Define RC Key for Equipment Operation
Select RC key from pull-down list
“_quantum” or “_astro” is reserved for Auto Stress Test Equipment Control Command
Define how many times this RC key is repeated
no repeat if empty
Define waiting duration before next RC key step
0 ms if empty
Select Timing from pull-down list
Change color space for Quantum, can select from pull-down list
set stream to play, click twice can fill stream name

## Slide 10: Define RC Key Operation
RC Key | Times | RC Repeat (ms) | … | Sys Delay (ms)
Menu | 1 |  | … | 300
Exit |  |  | … | 
Vol+ | 3 | 100 | … | 1000
Ch+ | 2 | 3000 | … | 300
Select RC key from pull-down list
“_cmd” is reserved for Auto Stress Test System Control Command
Define how many times this RC key is repeated
no repeat if empty
Define waiting duration after each RC key sent
0 ms if empty
Define waiting duration before next RC key step
0 ms if empty

## Slide 11: RC Key Operation Spec
Menu
RC Key | Times | RC Repeat (ms) | … | Sys Delay (ms)
Menu | 3 | 250 | … | 2000
Menu
Menu
NEXT RC

## Slide 12: Define System Control Operation
“_cmd” is System, ”_log1; _log2” for COMport use, not RC key
Take a picture
“_shot”
Record Video/Audio
“_start”, “_stop”
Record RS232 message, by “_save”
Clear message by “_clear”
Except with “_” prefix, all text is sent to TV, “Enter” key is added automatically
Waiting time
0 ms if empty
System Power
“_on”, “_off”

## Slide 13: Similarity Report Example
No. | Target | Source | Similarity | Sub-NG count | NG Rate | Result
1 | 1-1 | 2-1 | 80% | 1 | 1 | NG
2 | 1-2 | 2-2 | 90% | 0 | 0 | Pass
3 | 2-1 | 3-1 | 80% | 2 | 1 | NG
4 | 2-2 | 3-2 | 80% | 1 | 0.5 | NG
5 | 3-1 | 4-1 | 90% | 2 | 0.67 | Pass
6 | 3-2 | 4-2 | 90% | 1 | 0.33 | Pass
7 | 4-1 | 5-1 | 90% | 2 | 0.50 | Pass
8 | 4-2 | 5-2 | 90% | 1 | 0.25 | Pass
9 | 5-1 | 6-1 | 90% | 2 | 0.40 | Pass
10 | 5-2 | 6-2 | 90% | 1 | 0.20 | Pass
11 | 6-1 | 7-1 | 90% | 2 | 0.33 | Pass
12 | 6-2 | 7-2 | 90% | 1 | 0.17 | Pass
Target: Previous loop photo (click URL to pop image file)
Source: Current loop photo (click URL to pop image file)
Similarity: Target and source file to compare, similarity of Image Comparison.
2nd loop compare
3rd loop compare
4th loop compare
5th loop compare
6th loop compare
7th loop compare
1-1
2-1
80%
Target
Source
90%
1-2
2-2
Target
Source
Similarity default setting = 90%

## Slide 14: Similarity Report Example
No. | Target | Source | Similarity | Sub-NG count | NG Rate | Result
1 | 1-1 | 2-1 | 80% | 1 | 1 | NG
2 | 1-2 | 2-2 | 90% | 0 | 0 | Pass
3 | 2-1 | 3-1 | 80% | 2 | 1 | NG
4 | 2-2 | 3-2 | 80% | 1 | 0.5 | NG
5 | 3-1 | 4-1 | 90% | 2 | 0.67 | Pass
6 | 3-2 | 4-2 | 90% | 1 | 0.33 | Pass
7 | 4-1 | 5-1 | 90% | 2 | 0.50 | Pass
8 | 4-2 | 5-2 | 90% | 1 | 0.25 | Pass
9 | 5-1 | 6-1 | 90% | 2 | 0.40 | Pass
10 | 5-2 | 6-2 | 90% | 1 | 0.20 | Pass
11 | 6-1 | 7-1 | 90% | 2 | 0.33 | Pass
12 | 6-2 | 7-2 | 90% | 1 | 0.17 | Pass
Sub-NG count: Count the number of NG result
Sub-NG count_3= Sub-NG count_1 + Sub-NG count_3
Sub-NG count_5= Sub-NG count_1 + Sub-NG count_3 + Sub-NG count_5
NG Rate: The rate of Sub-NG count and Sub grand total
NG Rate_5 = Sub-NG count_5 / count(1,3,5) = 2/3 = 0.67
Result: Result of Image Comparison
2nd loop compare
3rd loop compare
4th loop compare
5th loop compare
6th loop compare
7th loop compare
Similarity default setting = 90%

## Slide 15: Trouble Shooting
Environment check:
  File path/directory path are correctly set
  Disable “Power saving” settings in PC/NB so that Auto Test won’t be affected by HD or peripheral power-down
I cannot find the RC key I need from pull-down list
  Please report to RC database administrator
No Response on TV
  Please make sure all indicators are correct
  Please make sure RC protocol is set correctly
RC Key operation is lost occasionally
  Duration of RC repeat and Sys delay should be sufficient for TV operation
  The response time of TV is various over different RC and TV models
  It is recommended to execute RC operation manually before setting RC repeat and Sys delay
Equipment connect to Auto box
  ASTRO VG871-B/ VG872-C and Quantum 882/ Dektec Gold-215

## Slide 16
Trouble Shooting
6. Multi Schedule:
  Can set 5 schedules in stress test
  Shorten the time
7. Mail system:
  When test finish can send Mail to personnel
8. Install:
  If you first install Auto Test program, please put config.ini and mail.ini file to Auto Test folder after install.
9. Time start:
  If program enable Start time of schedule, please don’t press “ START ”button, program will automatic start on set time.